## Slide 1: Jetson TX1 System for autonomous car

## Slide 2: Flash the OS
Once you fail to turn on the system, do this!

## Slide 3: Flash the OS
  Download Jetpack to a Ubuntu machine (this is the host machine)
  https://developer.nvidia.com/embedded/jetpack-notes
  Whenever possible, use the latest jetpack version
  Run jetpack, make sure your host machine are connected to the internet
  Takes about 4 hours
  Make sure you use force recover to turn on the board
    To check if it is successful, do lsusb on your host, you should see “Nvidia corp”

## Slide 4: Install OpenCV 3.4 for python 3
Please follow this link
  https://jkjung-avt.github.io/opencv3-on-tx2/ , https://jkjung-avt.github.io/tx2-camera-with-python/
cmake -D CMAKE_BUILD_TYPE=RELEASE -D CMAKE_INSTALL_PREFIX=/usr/local \
-D WITH_CUDA=ON -D CUDA_ARCH_BIN=“5.3" -D CUDA_ARCH_PTX="" \
-D WITH_CUBLAS=ON -D ENABLE_FAST_MATH=ON -D CUDA_FAST_MATH=ON \
-D ENABLE_NEON=ON -D WITH_LIBV4L=ON -D BUILD_TESTS=OFF \
-D BUILD_PERF_TESTS=OFF -D BUILD_EXAMPLES=OFF \
-D WITH_QT=ON -D WITH_OPENGL=ON ..
Take about 3 hours
sudo apt-get install gstreamer1.0-plugins-bad-faad \
gstreamer1.0-plugins-bad-videoparsers

## Slide 5: Run this code by python3 to test OpenCV installation
import cv2
import numpy as np
# Create a VideoCapture object and read from input file
# If the input is the camera, pass 0 instead of the video file name
cap = cv2.VideoCapture(1)
# Check if camera opened successfully
if (cap.isOpened()== False):
print("Error opening video stream or file")
# Read until video is completed
while(cap.isOpened()):
# Capture frame-by-frame
ret, frame = cap.read()
if ret == True:
# Display the resulting frame
cv2.imshow('Frame',frame)
# Press Q on keyboard to exit
if cv2.waitKey(25) & 0xFF == ord('q'):
break
# Break the loop
else:
break
# When everything done, release the video capture object
cap.release()
# Closes all the frames
cv2.destroyAllWindows()

## Slide 6: Install tensorflow 1.8 for python3
Download the wheel file here: https://devtalk.nvidia.com/default/topic/1031300/tensorflow-1-7-wheel-with-jetpack-3-2-/
Sudo pip3 install WHEEL_FILE_LOCATION

## Slide 7: Run this code to test installation
#!/bin/env python
import tensorflow as tf
state = tf.Variable(0, name="counter")
one = tf.constant(1)
new_value = tf.add(state, one)
update = tf.assign(state, new_value)
init_op = tf.global_variables_initializer()
with tf.Session() as sess:
# Run the 'init' op
sess.run(init_op)
# Print the initial value of 'state'
print (sess.run(state))
# Run the op that updates 'state' and print 'state'.
for _ in range(3):
sess.run(update)
print (sess.run(state))
input1 = tf.constant(3.0)
input2 = tf.constant(2.0)
input3 = tf.constant(5.0)
intermed = tf.add(input2, input3)
mul = tf.multiply(input1, intermed)
with tf.Session() as sess:
result = sess.run([mul, intermed])
print (result)
input1 = tf.placeholder(tf.float32)
input2 = tf.placeholder(tf.float32)
output = tf.multiply(input1, input2)
with tf.Session() as sess:
print (sess.run([output], feed_dict={input1:[7.], input2:[2.]}))

## Slide 8: Install Lidar (not successful yet)
https://blog.csdn.net/u013620235/article/details/70229272
https://devtalk.nvidia.com/default/topic/890599/?comment=4710941
https://gist.github.com/chutsu/9bb6abe6f61924c88521adec859c7006
https://stackoverflow.com/questions/23050188/cant-make-menuconfig

## Slide 9: Traffic light detection algorithm
Using pre-trained TF model
  http://download.tensorflow.org/models/object_detection/ssdlite_mobilenet_v2_coco_2018_05_09.tar.gz
Pre-trained ssd_mobilenet for traffic light detection
Image / Video frame
Traffic light location
Crop image
Red light / Green light locations
OpenCV to detect red/green color
No traffic light ahead

## Slide 10: Magenta line detection algorithm
In the current version, it is very simple
Just extract all the magenta colors
And use Pearson correlation to detect lines